## Slide 1: CompriVAP On the way to decarbonisation with waste heat utilisation on an industrial scale

## Slide 2
Globally acting, Austrian supplier of thermal separation and environmental technology
Our offering
Core competence: Design and manufacturing of falling-film, thin-film, short-path, distillation and drying technology
Technology for CO2 valorization and industrial heat pump solution
Projects ranging from pilot plants and skid units to turnkey plants on EPC basis
Own technical center for trials and R&D
GIG Karasek – Who we are
We are proud on our extensive knowhow, top-quality technology and highly committed employees. We have everything in our hands for supporting our customers and being a valued industry partner.”
Julia Aichhorn, General Manager
Our motto “Concentrating the Essentials” perfectly fits to our approach and way of working. We are focusing on utmost efficiency – both, in our core competences but also in new environmental technologies.”
Andreas Schnitzhofer, General Manager

## Slide 3
Dr. Aichhorn group
The Dr. Aichhorn Forestry Estate is sustainably managed according to the latest forestry knowledge available
Worldwide manufacturer and provider of high-pressure equipment and high-pressure components for the chemical and petrochemical industries
European producer of high-pressure pumps with operating pressures between 200 and 1,200 Mpa
Globally acting, Austrian supplier of thermal separation and environmental technology

## Slide 4
GIG Karasek – Our business units
Environmental Technologies
CO2 valorization and industrial heat pump technology for a sustainable economy
Thin-film and Short-path Technology
Different types of evaporators for complex tasks and tailored process solutions
Conventional Evaporation Technology
Different types of evaporators and tailor-made process solutions for
high evaporation rates
Technical Center
Laboratory tests, pilot test and scale up concepts for thermal separation and environmental technologies

## Slide 5
New business unit established in 2022
Focusing on
DEFOSSILIZATION
CO2 valorization = transformation of carbon dioxide into chemicals and fuels
DECARBONIZATION
Waste heat utilization by means of CompriVAP industrial heat pump solution
Environmental Technologies
GIG Karasek Team Environmental Technologies?

## Slide 6
Present problem
Exhaust steam and wastewater are typical waste heat streams
Largely not reused, although a significant amount of energy is still contained
Furthermore, cooling down/additional energy input is needed for environmental release
unused waste heat in industry
Renewable Energy Directive (RED III-EU/22023/2413)
§22a Mainstreaming renewable energy in industry
… Waste Heat can be included under conditions …

## Slide 7
WHY WASTE HEAT UTILIZATION?
Reuse waste heat
 Reduction of primary energy demand
 Significant reduction of CO2 emissions possible
Economic use of resources
 less fresh steam and cooling water demand
High potential of OPEX savings
NEED FOR WASTE HEAT UTILISATION

## Slide 8
A solution
Steam generation by industrial waste heat utilization

## Slide 9
MAIN FUNCTIONAL PRINCIPLE
Energy level of steam is raised by means of MVR (Mechanical Vapor Recompression) fans
Preconditions:
Sufficient low-pressure input medium available
Possible input: waste steam or warm liquid
Clearly defined output target
CompriVAP Industrial heat Pump Solution
Example: Industrial heat pump solution with Piller compressors
© Piller

## Slide 10
CompriVAP Industrial heat Pump Solution
VACUUM FLASH TANK
SOURCE
Warm liquids or vapours
HEAT EXCHANGER
Condensate return (e.g. closed media loop) or Make up water
Residual water
RECROMPRESSION FANS driven by green energy
OUTPUT STEAM
TO HEAT CONSUMER
OR STEAM NET
OPTIONAL Secondary media circuit working with demineralized water only
RETURN

## Slide 11
THERMODYNAMICALLY FAVORABLE CONDITIONS
Energy sources:
  Residual or surplus process vapors
  Hot water or other warm liquids
Steam generation:
  up to 215°C and 20 bar(g) possible
Compressor setup serial and / or parallel
No refrigerants used (!)
Thermodynamically favorable conditions
1
Flash tank
2
Compressors
> 70 °C
3
Heat exchanger
1
2
2
3

## Slide 12
Solution for Multiple Energy Sources
One single heat exchanger for multiple heat recovery

## Slide 13: Use Case - Heat Recovery Dryer Application (Small)

## Slide 14
Engineered application Dryer (SMALL)
VACUUM FLASH TANK
INPUT
Heat source: Warm water 72°C
Approx. 1,3 MW thermal power
HEAT EXCHANGER
Makeup water
Residual water
MULTIPLE VAPOR RECROMPRESSION
OUTPUT STEAM
REUSE as process steam for internal heating
Vacuum steam
> 2.600 kg/h
Steam duty > 1,56 MW up to 4,1 bara ~ 144°C
REQUIREMENTS
Reuse of warm water at >72°C
Thermal Power available at Input side approx. 1,3 MW
Generate process steam for an internal heating application
Make available >2500 kg/h steam at >144 °C saturated (4,1 bara)
Continuous operation over 350 days/a
Turn down ratio to <70%
RETURN
Warm water

## Slide 15
PROPOSED SOLUTION
9-stage CompriVAP system (Skid)
Layout on 2 levels to fit in existing brown field area
Solution with vacuum flash tank
Operation in partial-load possible (turn down ratio: <70%)
System is controlled by VSDs of the compressor motors
COP (shaft): >3,6
Engineered application Dryer (SMALL)
KEY PARAMETERS | 
Total installed electrical power: | 450 kW
Total operating power: | 416 kW
Total steam output (design value): | 2.600 kg/h
Discharge temp. saturated | 144 °C
Discharge pressure | 4132 mbar(a)

## Slide 16: Use Case - Heat Recovery Pulp Mill (Medium)

## Slide 17
CUSTOMER REQUIREMENTS
Reuse of warm water at 78°C
Generate process steam for an internal heating application
Make available 15,1 MW LP steam at 3,5 bara and 139 °C saturated
Continuous operation over 350 days/a
Turn down ratio to 70%
Engineered application Pulp mill (medium)

## Slide 18
Engineered application Pulp mill (medium)
VACUUM FLASH TANK
INPUT
Heat source: Warm water 78°C
HEAT EXCHANGER
Makeup water
Residual water
MULTIPLE VAPOR RECROMPRESSION FANS
OUTPUT STEAM
REUSE as process steam for internal heating
up to 3,5 bara at ~ 139°C
PROPOSED SCOPE OF SUPPLY
Engineering and design, procurement, delivery, installation, commissioning and start-up

## Slide 19
PROPOSED SOLUTION FOR USE CASE – 3,5 BAR
6-stage CompriVAP system
Layout on 2 levels to fit in existing brown field area
Solution with vacuum flash tank
Operation in partial-load possible (turn down ratio: 35%)
System is controlled by VSDs of the compressor motors
Engineered application Pulp mill (medium)
KEY PARAMETERS | 
Total installed electrical power: | 4,80 MW
Total operating power: | 4,07 MW
Total steam output (design value): | 25.333 kg/h
Discharge temp. saturated | 138,9 °C
Discharge pressure | 3504 mbar(a)

## Slide 20
Engineered application Pulp mill (medium)
COP COEFFICIENT OF PERFORMANCE |  | 
Massflow | Kg/h incl. injection | 25 333,0
Power shaft | kW | 3 862,6
Motor eff | % | 95,0
Electrical power | kW | 4065,9
Latent heat | kJ/kg at 3,37 bara | 2147,7
 | COP | 3,72
OPEX COMPARISON COSTS LIFE STEAM VS. ELECTRICITY |  |  | 
 |  | EXAMPLE 1 | EXAMPLE 2
Operation time | h/a | 8000 | 8000
Price LP steam* | EUR/t | 40 | 60
Costs/a LP steam | EUR/a | 8 106 560,00 | 12 159 840,00
Price electricity* | EUR/kWh | 0,1 | 0,1
Costs/a electricity | EUR/a | 3 252 715,79 | 3 252 715,79
Potential savings | EUR/a | 4 853 844,21 | 8 907 124,21
Potential savings | EUR/3a | 14 561 532,63 | 26 721 372,63
* Estimation depending on client conditions

## Slide 21: Use Case – Heat Recovery Industrial Application (Large)

## Slide 22
REQUIREMENTS
Reuse of warm water (>1500 t/h, @>72°C ) to generate process steam for the MP Steam line
Make available >60 t/h steam @ >5,5 bara
Use the CompriVAP process to increase the steam output pressure up to 6 bara saturated steam
Engineered Industrial application (large)

## Slide 23
Engineered Industrial application (large)
VACUUM FLASH TANK
Input
Warm water up to 72°C, 1500 t/h
HEAT EXCHANGER
Makeup water
Residual water
MULTIPLE VAPOR RECROMPRESSION FANS
OUTPUT STEAM
Feed into factory steam line or individual use
Vacuum steam
>60 t/h incl. injection water
up to 6 bara saturated steam
>35 MW steam duty and more possible
PROPOSED SCOPE OF SUPPLY
Engineering and design, procurement, delivery, installation, commissioning and start-up
Warm water
Return

## Slide 24
PROPOSED SOLUTION FOR USE CASE
11-stage CompriVAP system
Layout on 1 level
Solution with vacuum flash tank
Operation in partial-load via bypass (turn down 50%)
System is controlled by VSDs of the compressor motors
COP >3,3 possible
use case – Industrial application (large)

## Slide 25: A common project

## Slide 26
HOW WE SUPPORT YOU
Detailed evaluation of available waste heat
Tailored process design comprising open or partly open process circuits
Careful selection of compressors from different OEMs
Detailed planning of necessary compression stages
Fact-based evaluation of CAPEX and OPEX aspects
CompriVAP Industrial heat Pump Solution

## Slide 27
SCOPE OF SUPPLY: TURNKEY
Process design
Basic- and Detail engineering
Compressors, auxiliary equipment, spare parts
Vapor ducts and piping
Flash tank (if needed)
Instrumentation
Installation and supervision
Commissioning and startup support
CompriVAP Industrial heat Pump Solution

## Slide 28
Reference highlight – MVR technology
SAPPI SAICCOR, South Africa | 
Application | Sulphite spent liquor
Scope | 300 t/h water evaporation 16 MW installed power
HIGHLIGHT | Largest MVR evaporation plant for sulphite liquor EPC delivery: MVR plant and tank farm (2018-2021)

## Slide 29
Josef Grassauer
+43 664 8218703
j.grassauer@gigkarasek.at